## Slide 1: LiDAR in Remote Sensing: From Traditional Methods to Deep Learning (A brief intro)
Dr. Fei Zhang
04/22/2025

## Slide 2: Quiz
1. Which of the following movie scenes best resembles how real LiDAR technology works today (in 2025)?
Rogue One: A Star Wars Story (2016) https://www.google.com/url?sa=i&url=https%3A%2F%2Fimgur.com%2Fgallery%2Fhopes-class-4-5-beam-laser-5Eew4mn&psig=AOvVaw0-xvKURfgtF4XW6WxwtLC3&ust=1745346703064000&source=images&cd=vfe&opi=89978449&ved=0CBQQjhxqFwoTCJDFlbbl6YwDFQAAAAAdAAAAABAE
B. Tron (1982)
https://www.google.com/url?sa=i&url=https%3A%2F%2Fsci-fi-gifs.tumblr.com%2Fpost%2F768995527999242240&psig=AOvVaw0-xvKURfgtF4XW6WxwtLC3&ust=1745346703064000&source=images&cd=vfe&opi=89978449&ved=0CBQQjhxqFwoTCJDFlbbl6YwDFQAAAAAdAAAAABAJ
C. Ocean's Twelve (2004) https://www.google.com/url?sa=i&url=https%3A%2F%2Fmakeagif.com%2Fgif%2Foceans-twelve-laser-dance-hd-1080p-S62pot&psig=AOvVaw1pECVATbn8HYooQs8tgUll&ust=1745347449767000&source=images&cd=vfe&opi=89978449&ved=0CBQQjhxqGAoTCMCAk4jk6YwDFQAAAAAdAAAAABDpAQ
Notes: A. a space weapon
B. a 3D scan device
C. a security system.

## Slide 3: Quiz
2. What does the LiDAR on an iPhone 12 Pro do?
Faster and sharper photos in low light
Room scanning and measurements
Augmented Reality (AR)
Notes: A. It improves focus and portrait effects in night mode by understanding depth better.
B. Apps like Measure or IKEA Place use LiDAR to accurately measure spaces and objects.
C. AR apps (like those from IKEA, Snapchat, or games) can anchor virtual objects more realistically in your environment.

## Slide 4: Quiz
3. If you were building a robot to explore a dense, dark forest, which tool would help it "see" and safely find its way through?
A flashlight and a stick
B. A 2D camera with night vision
C. A LiDAR scanner
Notes: A flashlight and a stick - to poke around and light the way, one step at a time
A 2D camera with night vision – to take flat images, even in low light
A LiDAR scanner – to scan the surroundings and build a 3D map in real time

## Slide 5: Outline
1. Introduction to LiDAR and Remote Sensing
2. Traditional Point Cloud Techniques
1. Noise Filtering - SOR vs ROR
2. Ground Filtering - Cloth Simulation Filter
2. Feature Extraction & Structural Analysis
3. Classification and Segmentation (non-DL)
4. Point Cloud Registration - ICP
3. Deep Learning for LiDAR
1. Motivation: Why DL?
2. Historical Context
3. PointNet
4. Practical Considerations
4. Explainability in DL
5. Summary & Future Directions + Quick Q&A

## Slide 6: What is LiDAR
An example of airborne LiDAR ref:https://www.geoilenergy.com/en/servicios/geoespaciales/eagle-mapping

## Slide 7: What is LiDAR
ref: https://www.laserscanningforum.com/forum/viewtopic.php?t=17157
Why lasers?
Notes: Why lasers? Why not just a normal lights, like LEDs, or flashlights?
highly coherent vs incoherent
very directional vs spread out
single wavelength vs wide range of wls

## Slide 8: Laser Beam Divergence
ref: Lidar beam divergence and footprint – Geohub
https://www.google.com/url?sa=i&url=https%3A%2F%2Fgeohubkenya.wordpress.com%2F2019%2F05%2F17%2Flidar-beam-divergence-and-footprint%2F&psig=AOvVaw2B8qdWc1i0c_nJwgIwaAsx&ust=1745336595315000&source=images&cd=vfe&opi=89978449&ved=0CBcQjhxqGAoTCJiZudC76YwDFQAAAAAdAAAAABCZAQ
ref: https://web.phys.ksu.edu/VQM/laserweb/Labs/Diverge/Cdiverge2.htm

## Slide 9: LiDAR on different platforms
Illustration of the various remote sensing platforms for forest structure measurements. Borsah, A. A., Nazeer, M., & Wong, M. S. (2023). LIDAR-Based Forest Biomass Remote Sensing: A Review of Metrics, Methods, and Assessment Criteria for the Selection of Allometric Equations. Forests, 14(10), 2095. https://doi.org/10.3390/f14102095
Why multiple returns?

## Slide 10: LiDAR on Autonomous Vehicles
An example LiDAR point cloud on Self-Driving Cars. https://www.google.com/url?sa=i&url=https%3A%2F%2Fmedium.com%2F%40BabakShah%2Flidar-in-self-driving-cars-cee29db94af7&psig=AOvVaw2LzjL5ysaiZHlerfRnxv_B&ust=1745345894988000&source=images&cd=vfe&opi=89978449&ved=0CBQQjhxqFwoTCJiYo6be6YwDFQAAAAAdAAAAABA5

## Slide 11: Why LiDAR - applications
Autonomous vehicles (cars, delivery bots)
Drone mapping (precision agriculture, inspection)
Forestry terrain & canopy structure
Warehouse robots (AMRs, AGVs)
Construction site monitoring
3D modeling of indoor spaces (real estate)
…
Anymore?
Notes: robot vacuum
robot mower

## Slide 12: LiDAR in Forestry
A typical workflow to derive forest information. https://en.wikipedia.org/wiki/Lidar

## Slide 13: Traditional Point Cloud Techniques
Preprocessing and filtering
  SOR
  ROR
  Ground filtering - CSF

## Slide 14: Statistical Outlier Removal (SOR)
Principle:
SOR identifies noisy points based on statistical analysis of the distances between each point and its neighbors.
Steps:
Define a neighborhood: For each point, find its k nearest neighbors (typically k=20–50).
Calculate the mean distance: Compute the mean distance from this point to its neighbors.
Identify outliers: Points whose mean distances exceed a threshold (typically defined as a mean distance plus a multiple of standard deviations) are considered outliers and are removed.
Typical Parameters:
Number of Neighbors (k): Determines the neighborhood size.
Standard Deviation Multiplier (std): Points with mean distances greater than mean + std × σ are removed.
How to calculate the distance_matrix?

## Slide 15: Statistical Outlier Removal (SOR)
Principle:
SOR identifies noisy points based on statistical analysis of the distances between each point and its neighbors.
Steps:
Define a neighborhood: For each point, find its k nearest neighbors (typically k=20–50).
Calculate the mean distance: Compute the mean distance from this point to its neighbors.
Identify outliers: Points whose mean distances exceed a threshold (typically defined as a mean distance plus a multiple of standard deviations) are considered outliers and are removed.
Typical Parameters:
Number of Neighbors (k): Determines the neighborhood size.
Standard Deviation Multiplier (std): Points with mean distances greater than mean + std × σ are removed.

## Slide 16: Radius Outlier Removal (ROR)
Principle:
ROR removes points based on the number of neighboring points within a fixed radius.
Steps:
Define a radius (r): Choose a spherical neighborhood radius around each point.
Count neighbors: For each point, count how many neighbors fall within this radius.
Identify outliers: If the number of neighbors within the radius is below a specified threshold, the point is considered an outlier and removed.
Typical Parameters:
Radius (r): Defines the neighborhood search radius.
Minimum Neighbor Count: Minimum number of neighbors required to keep a point.

## Slide 17: SOR vs ROR
Feature | SOR | ROR
Neighborhood Definition | k-nearest neighbors | Fixed radius neighbors
Outlier Criterion | Mean distance + std deviation | Neighbor count within radius
Density Adaptivity | Good for variable densities | Less adaptive; better for uniform densities
Parameter Sensitivity | Moderate | High
Computational Cost | Moderate (fast with k-d trees) | Moderate to High (depends on radius and density)
Notes: Practical Recommendations:
Use SOR when dealing with variable point cloud densities or unknown density distributions.
Use ROR when point cloud density is relatively uniform or you clearly understand your data's spatial distribution.
Both filters are commonly available in libraries such as PCL (Point Cloud Library) and Open3D.

## Slide 18: Preprocessing and filtering
Ground filtering - Cloth Simulation Filter
Zhang, W., Qi, J., Wan, P., Wang, H., Xie, D., Wang, X., & Yan, G. (2016). An Easy-to-Use Airborne LiDAR Data Filtering Method Based on Cloth Simulation. Remote Sensing, 8(6), 501. https://doi.org/10.3390/rs8060501
Overview of the cloth simulation algorithm.
Main Steps in CSF: (a) Initial state. A cloth is place above the inverted LiDAR measurements; (b) The displacement of each particle is calculated under the influence of gravity. Thus, some particles may appear under the ground measurements; (c) Intersection check. For those who are under the ground, they are moved on the ground and set as unmovable; (d) Considering internal forces. The movable particles are moved according to forces produced by neighbour particles.

## Slide 19: PCA for normals and others
My previous slides.

## Slide 20: Deep Learning for LiDAR

## Slide 21: Motivation: Why Deep Learning?
Superior Performance on Complex Tasks
Automatic feature learning (vs hand-crafted)
End‑to‑End Training and Task Specialization
  no more parameters tuning once the model is built.

## Slide 22: Early DL Methods on Point Clouds
Initial attempts: Voxel-based methods (~2015)
Multi-view methods (~2016)
Emergence of point-based methods (~2017-present)

## Slide 23: Early DL Methods on Point Clouds: Historical Context
Initial attempts: Voxel-based methods (~2015)
Maturana, D., & Scherer, S. (2015, September). Voxnet: A 3d convolutional neural network for real-time object recognition. In 2015 IEEE/RSJ international conference on intelligent robots and systems (IROS) (pp. 922-928). IEEE. Citation: 4449 (as of 04/19/2025)

## Slide 24: Early DL Methods on Point Clouds
Multi-view methods (~2016)
Projecting point clouds to multiple 2D views (MVCNN)
Advantages (leveraging mature CNN architectures)
Limitations (loss of geometric detail, computational inefficiency)
Su, H., Maji, S., Kalogerakis, E., & Learned-Miller, E. (2015). Multi-view convolutional neural networks for 3d shape recognition. In Proceedings of the IEEE international conference on computer vision (pp. 945-953). Citations: 4412 as of 04/19/2025

## Slide 25: Challenges for direct point-based learning
Bello, S. A., Yu, S., Wang, C., Adam, J. M., & Li, J. (2020). Review: Deep Learning on 3D Point Clouds. Remote Sensing, 12(11), 1729. https://doi.org/10.3390/rs12111729

## Slide 26: Early DL Methods on Point Clouds
Emergence of point-based methods (~2017-present)
Qi, C. R., Su, H., Mo, K., & Guibas, L. J. (2017). Pointnet: Deep learning on point sets for 3d classification and segmentation. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 652-660).
Cited by 19544

## Slide 27: Pointnet
Emergence of point-based methods (~2017-present)
Qi, C. R., Su, H., Mo, K., & Guibas, L. J. (2017). Pointnet: Deep learning on point sets for 3d classification and segmentation. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 652-660).
Cited by 19544
Notes: t an affine transformation matrix by a mini-network (T-net) The first transformation network is a mini-PointNet that
takes raw point cloud as input and regresses to a 3 3
matrix. It’s composed of a shared MLP(64; 128; 1024)
network (with layer output sizes 64, 128, 1024) on each
point, a max pooling across points and two fully connected
layers with output sizes 512, 256. The output matrix is
initialized as an identity matrix. All layers, except the last
one, include ReLU and batch normalization.

## Slide 28: Deep Dive into PointNet - Affine transformation matrix
affine-transformation-mathworks
Notes: t an affine transformation matrix by a mini-network (T-net)

## Slide 29: Deep Dive into PointNet - T-Net
Emergence of point-based methods (~2017-present)
Qi, C. R., Su, H., Mo, K., & Guibas, L. J. (2017). Pointnet: Deep learning on point sets for 3d classification and segmentation. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 652-660).
Cited by 19544
Notes: Why is T-Net?

## Slide 30: Canonicalization - How PointNet Learns Transformations
“canonicalize the data”
“sort input into a canonical order”
“align all input set to a canonical space”
Notes: Canonicalization - To canonicalize something means to transform it into a standard, consistent, or normalized form — so that it's easier to process, compare, or analyze.
Think of it as saying:
“No matter how the input is rotated, flipped, or scaled, let’s rearrange it to a standard version, so we can recognize it.”

## Slide 31: Canonicalization - How PointNet Learns Transformations
Emergence of point-based methods (~2017-present)
Qi, C. R., Su, H., Mo, K., & Guibas, L. J. (2017). Pointnet: Deep learning on point sets for 3d classification and segmentation. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 652-660).
Cited by 19544
The first transformation network is a mini-PointNet designed to process raw point clouds.
Its goal is to regress to a 3×3 transformation matrix.
Architecture components:
  Shared MLP layers on each point with output sizes: 64 → 128 → 1024.
  Max pooling is applied across all points.
  Followed by two fully connected layers with output sizes: 512 → 256.
The output is a 3×3 matrix, initialized as the identity matrix.
All layers except the last use ReLU activation and batch normalization.
Notes: But wait, why 3x3? not 4x4? This is a linear transformation:
Includes rotation
scaling
shearing
possibly reflection
But it does not include translation.

## Slide 32: Canonicalization - How PointNet Learns Transformations
Qi, C. R., Su, H., Mo, K., & Guibas, L. J. (2017). Pointnet: Deep learning on point sets for 3d classification and segmentation. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 652-660). Cited by 19544
https://github.com/yanx27/Pointnet_Pointnet2_pytorch
The first transformation network is a mini-PointNet designed to process raw point clouds.
Its goal is to regress to a 3×3 transformation matrix.
Architecture components:
  Shared MLP layers on each point with output sizes: 64 → 128 → 1024.
  Max pooling is applied across all points.
  Followed by two fully connected layers with output sizes: 512 → 256.
The output is a 3×3 matrix, initialized as the identity matrix.
All layers except the last use ReLU activation and batch normalization.
Notes: But wait, why 3x3? not 4x4? This is a linear transformation:
Includes rotation
scaling
shearing
possibly reflection
But it does not include translation.

## Slide 33: Time and Space Complexity Analysis
Qi, C. R., Su, H., Mo, K., & Guibas, L. J. (2017). Pointnet: Deep learning on point sets for 3d classification and segmentation. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 652-660). Cited by 19544
Notes: But wait, why 3x3? not 4x4? This is a linear transformation:
Includes rotation
scaling
shearing
possibly reflection
But it does not include translation.

## Slide 34: PointNet

## Slide 35: More to come
KPConv
DGCNN
PointGPT
…

## Slide 36: Practical Considerations
Deep learning algorithms are cool …
… until they are out of control.

## Slide 37: Practical Considerations
Data Preparation
Garbage in, garbage out: DL models like PointNet are highly sensitive to noisy or inconsistent input data.
Uniform Sampling Needed: PointNet requires fixed-size point sets (e.g., 1,024 points)—need to downsample or pad each point cloud.
Normalization is Critical: Inputs must be centered and scaled to unit spheres—forgetting this leads to unstable training.
Class Imbalance Hurts: Forest scenes with mostly background or ground points can bias models—oversampling or weighted losses may be needed.
Noisy Annotations Break Learning: Manual segmentation errors or weak ground truth can severely hurt generalization.
Training Strategies
Overfitting Is Easy: Especially with small datasets—DL models memorize rather than learn unless regularized.
Data Augmentation Is Essential: Random rotations, jittering, and scaling help simulate variability and improve generalization.
Batch Normalization Matters: PointNet relies on batch norm to stabilize learning; small batch sizes (due to GPU limits) may cause instability.
Custom Loss Functions Often Needed: Cross-entropy alone may not handle spatial smoothness—IoU loss or auxiliary losses can help.

## Slide 38: Find the Code, Send me a Message, and More…
https://github.com/fz-rit/TLS-showcase
https://github.com/fz-rit/LiDAR-session

## Slide 39: Backup Slides

## Slide 40: Feature Extraction & Structural Analysis
PCA & Surface Normals
RANSAC Shape Detection

## Slide 41: Normals Estimation with PCA
For each point in the point cloud:
  Find its k-nearest neighbors (commonly k = 10 ~ 30, depending on point density).
  Subtract the centroid of the neighborhood to center the points.
  Compute the covariance matrix of the neighbors.
  Use eigen decomposition (or SVD) on the covariance matrix.
  The eigenvector corresponding to the smallest eigenvalue is the estimated normal direction (it's perpendicular to the best-fit plane).
(Optional) Flip normals to point outward consistently:
  This is often done using viewpoint-based orientation or a Minimum Spanning Tree (MST) approach.

## Slide 42: RANSAC (RANdom SAmple Consensus)
Randomly selects a small subset of data.
Fits a model to this subset.
Tests how many other data points fit this model within a certain tolerance (called inliers).
Repeats the process a fixed number of times and keeps the model with the most inliers.

## Slide 43: RANSAC for Tree Shape Detection
Randomly selects a small subset of data.
Fits a model to this subset.
Tests how many other data points fit this model within a certain tolerance (called inliers).
Repeats the process a fixed number of times and keeps the model with the most inliers.

## Slide 44: Classification and Segmentation (non-DL methods)
Voxel based method
  Basic idea: Use voxel grids to summarize vertical and horizontal distributions of LiDAR returns, providing ecological insights.
  Example method: Vertical voxel profiling:
    Vertical distribution of point density/intensity within each horizontal voxel analyzed.
    Used to identify canopy layers, forest structure, or biomass estimation.
  Typical Applications:
    Forest canopy structure assessment.
    Biomass estimation and ecological modeling.
Region grow
  Region-growing segmentation involves starting from one or more "seed" points and progressively adding neighboring points that satisfy certain similarity criteria (such as geometric similarity, curvature, normal vectors, or intensity). This iterative expansion continues until no more suitable neighboring points can be added.
Notes: dea:
Start from "seed points" and iteratively expand regions based on local geometric similarity (e.g., normal vectors, curvature, intensity).
Examples:
Tree crown extraction (starting from tree-tops).
Building segmentation (expanding planar surfaces).
Strengths:
Efficient for structured environments, intuitive process.
Limitations:
Sensitive to parameters, may require manual tuning.

## Slide 45: Classification and Segmentation (non-DL methods)
Statistical & Machine Learning Approaches (traditional ML, not DL)
Idea:
  Traditional ML classifiers like Support Vector Machines (SVM), Random Forests (RF), or Decision Trees using handcrafted geometric features.
Examples:
  Point-level classification (e.g., ground, vegetation, urban structures).
  Urban or forestry applications using carefully extracted point-features.
Strengths:
  Relatively powerful, interpretable, well-established.
Limitations:
  Requires extensive feature engineering; performance heavily depends on quality of features.
Notes: dea:
Start from "seed points" and iteratively expand regions based on local geometric similarity (e.g., normal vectors, curvature, intensity).
Examples:
Tree crown extraction (starting from tree-tops).
Building segmentation (expanding planar surfaces).
Strengths:
Efficient for structured environments, intuitive process.
Limitations:
Sensitive to parameters, may require manual tuning.

## Slide 46: Point Cloud Registration & Alignment

## Slide 47: Point Cloud Registration & Alignment
Iterative Closest Point (ICP)